## Slide 1: Out of Order Pipeline
Reorder Buffer (ROB)
Write
back
Fetch
Decode
Execute
Commit
Register Alias Table (RAT)
FE_Latch
ID_Latch
SC_Latch
EX_Latch
All boxes in Red have to be implemented by students for the Lab
Sche-
dule
Issue

## Slide 2: Register Alias Table (RAT)
The number of entries in the RAT is equal to the number of ARF registers
Each entry has a valid bit and the id of the physical register
  If the RAT entry is invalid, it means that the register is not renamed and the value is present in the Architectural Register File (ARF)
  If the entry is valid, the PRF id is the index into the ROB ("tag" of the reservation stations -- “data in ROB” design)
The RAT needs to provide the following functions
During Issue:
  Get the PRF corresponding to the instruction's ARF sources
  Set the PRF for the instruction's ARF destination
During Commit:
  Reset (i.e., valid = 0) for ARF destination
ARF_ID | valid | PRF_ID
1 |  | 
2 |  | 
3 |  | 

## Slide 3: Reorder Buffer (ROB)
Each entry has a valid bit, exec bit, tags and presence (i.e., ready) bits for two sources (p1, src1 and p2, src2), the destination ARF and a ready bit for the destination.
We use the "data in ROB + separate ARF" implementation from the lectures. The index of the ROB is the renamed PRF_ID (or tag) for the destination ARF id, thus a separate “PRd” field is not needed. A "data" field for the destination is also not needed, as our simulator does not keep track of values.
For simplicity, we do not worry about any rollbacks due to exceptions/mis-speculations for this lab. Thus the LPRd (last name of the physical reg Rd) need not be stored here like we did in class.
The ROB contains a head pointer (pointing to the oldest uncommitted instruction) & a tail pointer (pointing to where a new instruction can be allocated).
PRF_ID | valid | exec | op | p1 | src1 (PRF id) | p2 | src2 (PRF id) | dest (ARF id) | ready
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 

## Slide 4: ROB (cont’d)
During Issue:
A new entry is allocated to the ROB, and the tail moves. The entry is marked as valid (use=1).
During Schedule:
When a valid entry has both sources ready (i.e., p1 and p2 are both true), it is scheduled and exec becomes 1.
During Writeback:
When an instruction completes execution, the ready bit for the destination in the ROB is marked 1.
During Commit:
If the oldest entry is valid and ready, it is removed from the ROB and committed.

## Slide 5: ROB (cont’d)
The ROB needs to provide the following functions:
  Check if there is space in the ROB
  Ability to insert an entry in the ROB
  Ability to execute (changing from exec=0 to exec=1)
  Ability to wake up waiting instructions on a matching writeback (and mark p*=1)
  Ability to mark an ROB entry as ready
  Ability to check if the head entry is valid and ready
  Ability to remove the head entry if it is valid and ready

## Slide 6: Given Pipeline Stages: IF, ID, EX
Instruction FETCH (IF): Fetches the instruction and passes it to the decode stage. Note that we are assuming perfect branch prediction. So, we do not need to account for control flow stalls.
Instruction DECODE (ID): Decodes the instruction and passes it to the issue stage. Note that we are not doing any dependency check in this stage. Dependencies are taken care of later in the pipeline.
Execution Stage (EXE): Takes the instruction from the SC_latch and transfers it to the EX_latch. However, we also need to support multi-cycle instructions. We handle this by having a waiting queue (EXEQ) that buffers waiting instructions and tracks their wait times. Once an instruction’s wait time reaches zero, it is transferred to the EX_latch.
NOTE: Our code base already has the above three stages implemented. So, you will need to focus on implementing only the stages new to the out-of-order pipeline.

## Slide 7: New Pipeline Stage: Issue
Insert new instruction into the ROB
  Check if the ROB is not full
  Insert the instruction
  Get remapped sources using RAT
    If the RAT entry is invalid, mark the source as ready
    If the RAT entry is valid, get the source ready bits from the ROB
  Get the index (i.e., PRF_ID) of ROB entry. This is the new map for the dest reg
  Update RAT with destination register map

## Slide 8: New Pipeline Stage: Schedule
Find up to N instructions ready to execute (N = pipeline width)
You will implement two scheduling policies:
In-order
Check if the oldest instruction in the ROB is ready (and unscheduled)
  If yes, schedule it
  If not, stall
Out of Order
Obtain a list of all instructions for which both sources are ready, and the instruction is unscheduled
Find the oldest instruction in this list and schedule it

## Slide 9: New Pipeline Stage: Writeback
For all instructions out of the EX stage (these can be > than pipeline width)
Broadcast the results to all the entries in the ROB
  This should wake up any sources waiting for this particular tag
Mark the ROB entry as ready

## Slide 10: New Pipeline Stage: Commit
Check the head of the ROB to see if it is ready
If yes, commit that instruction, update the stats, halt the pipeline if needed
Remove the instruction from the ROB, which will increment the ROB head
Update the RAT